Seoul National University NAS Parallel Benchmarks (SNU NPB) parallelisability study

BT
Almost all loops resemble each other very closely. There are some sequential while loops in the main() function of bt.c file, which operate with sequential input and output streams.
There are unrolled-like loop source code snippets in files solve_subs.c, set_constants.c. Compiler replaces these unrolled regions with memcopy or with loops, which it cannot ultimately parallelise.
Files x_solve.c, y_solve.c, z_solve.c consist of identical loops, which operate on different multi-dimensional arrays in a parallel fashion. Parallelisability is only constrained by the function calls present in the loop bodies. Function inlining techniques turn all these massive loops into parallelisible ones.

CG
CG benchmark has a more diverse loops with minimal amount of function calls in loop bodies. Loop parallelisability is constrained by irregular array accesses. Array pointing indecies are loaded from the memory and hence introduce all kinds of (true, anti, output) dependencies between may-intersect iterations. Another complicating factor in the benchmark is the while loops with unidentified control condition.
There are loops with cross iteration dependencies as well in this benchmark. Loops which are not parallelised by intel compiler because, they are considered to have too complex control flow and are not a parallelisation candidates. Loop with multiple exits cannot be vectorized. Could not identify loop control variable.

DC (Data Cube operator)
Horrible loops.
DC benchmark has loops printing standard output hence sequential. Loops, where it is hard to compute iteration count before executing the loop. While loops, where it is hard to indentify control variable and compute iteration count before loop execution. Loops, which contain irregular memory loads and stores to arrays. Loops with multiple exits.
Parallelisible loop adc.c(191) escapes compiler analysis. Compiler cannot compute iteration count.
Loop contains switch statement with function calls inside. Hence was not vectorized.
adc.c is really probematic from parallelisation point of view.

DC/extbuild.c(672)

ICC cannot vectorize the loop extbuild.c(672), because it cannot compute the amount of iterations. There are loops with statically unknown number of iterations.
There are while loops working with the standard output streams in extbuild.c(672). In some places like extbuild.c(970) compiler can determine loop iteration count
There are loops in DC/extbuild.c file with control conditions like i<adccntlp→nm, which in some cases escape vectorization due to unknown iteration count, and in some cases not.

DC/jobcntl.c(672)

EP
EP benchmark has loops with multiple exits (through break statement), which escape vectorization.

IS
IS benchmark has some loops, which compiler does not parallelise due to insufficient computational work. There are loops, which are generally not parallelisible, but have openmp pragma added in front of them, due to programmers specific knowledge (that some pointers do not alias, arrays contain certain types of values in indirect indexing, etc.) .

IS benchmark contains a lot of loops with #openmp pragmas added in front of them, but even for a reader with a human comprehension it is not clear, that these loops are parallelisible.

LU
LU benchmark